E G S PILLAY ENGINEERING COLLEGE, NAGAPATTINAM

DEPARTMENT OF CIVIL ENGINEERING

CE6412-HYDRAULIC ENGINEERING LAB

II YEAR - IV SEM

|  | CONTENTS |
| --- | --- |
| S.NO | LIST OF EXPERIMENTS |
| 1 | CALIBRATION OF ROTAMETER |
| 2 | FLOW THROUGH VENTURIMETER |
| 3 | FLOW THROUGH ORIFICEMETER. |
| 4 | FLOW THROUGH VARIABLE DUCT AREA-BERNOULLI’S EXPERIMENT |
| 5 | FLOW THROUGH RECTANGULAR NOTCHE |
| 6 | FLOW THROUGH TRIANGULAR NOTCHE |
| 7 | DETERMINATION OF FRICTION CO EFFICIENT IN PIPES |
| 8 | CHARACTERISTIC OF CENTRIFUGAL PUMPS |
| 9 | CHARACTERISTIC OF RECIPROCATING PUMPS |
| 10 | CHARACTERISTIC OF GEAR PUMPS |
| 11 | CHARACTERISTIC OF PELTON WHEEL TURBINES |
| 12 | CHARACTERISTIC OF FRANCIS TURBINES |
| 13 | CHARACTERISTIC OF KAPLAN TURBINES |

CALIBRATION OF ROTAMETER

EXP NO: 01

DATE:

AIM

To determine the percentage error in Rotameter with the actual flow rate.

APPARATUS REQUIRED

1. Rotameter (0 – 10 LPM range)

2. Single phase mono block pump set (0.5 HP, 1440 RPM)

3. Reservoir tank arrangement.

- Measuring tank arrangement.

- Piping System ‘

PROCEDURE

- Switch on the motor and the delivery valve is opened

- Adjust the delivery valve to control the rate in the pipe

3. Set the flow rate in the Rotameter, for example say 50 liters per minute 4. Note down the time taken for 10 cm rise in collecting tank

5. Repeat the experiment for different set of Rotameter readings 6. Tabular column is drawn and readings are noted

7. Graph is drawn by plotting Rotameter reading Vs percentage error of the Rotamete]

FORMULAE

ACTUAL DISCHARGE

Actual rate of flow Qact = Ah/t m3/sec

Where A = Area of the measuring tank in ‘m2 ‘ h = Difference in levels of water in ‘m’ x (10- 2)

t = Time taken for 10 cm rise of water level in collecting tank in ‘Seconds’

CONVERSION

Actual flow rate (lit / min), Qact = Qact x 1000 x 60 lit /min

Percentage error of Rotameter =

Rotameter reading ~ Actual/ Rotameter readihg x 100 % = (R ~ Qact )/ R x 100

GRAPH:

Rotameter reading Vs percentage error

ROTAMETER APPARATUS

Internal area of measuring tank = 0.3 x 0.2 m2.

| Sl | Rotameter reading | Time taken For | Actual | Co-efficient of | Percentage |
| --- | --- | --- | --- | --- | --- |
| No. | (Theoretical | 50mm Rise sec | discharge(m3/sec) | discharge | Error of |
|  | discharge) LPM |  |  | Cd | Rotameter |
|  |  |  |  |  | (%) |
| 1 |  |  |  |  |  |
| 2 |  |  |  |  |  |
| 3 |  |  |  |  |  |
| 4 |  |  |  |  |  |
| 5 |  |  |  |  |  |

RESULT

The percentage error of the Rotameter was found to be………….….%

FLOW THROUGH VENTURIMETER

EXP NO: 2

DATE:

AIM:

To determine the coefficient of discharge for liquid flowing through venturimeter.

APPARATUS REQUIRED

1) Venturimeter

2) Piping system

3) Measuring tank

4) Sump tank

5) Differentia Manometer

6) Supply pump set

PROCEDURE

- While taking reading, close all the Ball valves in the pressure feed pipes except the two (downstream and upstream) Ball valves which directly connect the manometer to the required flow meter for which the differential head is to be measured.

2) Make sure while taking reading that the manometer is properly primed.

3) Priming is the operation of filling the upper part of the manometer and the connecting pipes with water and venting air from the pipes.

4) First open the inlet gate valve of the apparatus.

5) Adjust the control valves kept at the exit end of the apparatus to a desired flow rate and maintain the flow steadily.

6) Note the time required for 100mm rise in measuring tank and manometer reading.

7) Take reading for different flow rates

FORMULA

ACTUAL DISCHARGE

Actual rate of flow Qa = Ah/t m3/sec

`	Where A = Area of the measuring tank in ‘m2 ‘

h = Difference in levels of water in ‘m’ x (13.6 - 1) t = Time in ‘seconds’

THEORITICAL DISCHARGE

The Theoretical discharge through an orifice meter is given by the following formula. Qt= k √H m3/sec. The above equation is simplified from the formula.

Qt= a1a2√2gH/√ a12a22

Where a2√2g/√1-m2

a2= Area of Orifice in ‘m2’ m = Area ratio = a2/a1

h = Differential head of manometer in ‘meters’ g = Acceleration due to gravity (9.81m/sec2) a1= Inlet Area of Venturimeter in ‘m

CO-EFFICIENT OF DISCHARGE

Co- efficient of discharge = Q a / Q t (no units)

The venturimeter is designed for the following area and diameter ratios

The flow constants are given below for the venturimeter.

| Venturimeter Size (mm) |  |  | Throat dia (mm) |  |  | Flow constant (k) |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 25 |  |  |  |  | 14.79 |  |  | 8.12 x 10-4 |  |  |
| Sl |  | Manometer |  | Manometer Head | Time | Actual | Theoretical | Co- |
| No |  | Reading |  | ‘h’ | for | discharge | Discharge | efficient of |
|  |  | (mm of hg) |  | m of water | 100m | Qa | Qt | discharge |
|  |  |  |  |  |  | rise ‘t’ | m2/sec | m2/sec | cd |
|  |  |  |  |  |  | sec |  |  |  |  |  |
| 1 | h1 | h2 | hm |  |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | average |  |  |

VENTURIMETER TEST RIG DETAILS

Size of Venturimeter d1 = 25mm

Throat diameter d2 = 14.79mm

Area ratio a2/a1 = 0.35

Measuring area in collecting tank A = (0.3 x 0.3) m2

Kvalue=a2√2g/√1-m2

RESULT

The co efficient of discharge through Venturimeter is ………

FLOW THROUGH ORIFICEMETER

EXP NO: 03

DATE:

AIM

To determine the co-efficient discharge through orifice meter

APPARATUS REQUIRED

- Orifice meter

- Piping system.

- Measuring tank.

- Sump tank.

- Differential Manometer.

- Supply pump set.

PROCEDURE

`1) While taking reading, close all the Ball valves in the pressure feed pipes except the two (downstream and upstream) Ball valves which directly connect the manometer to the required flow meter for which the differential head is to be measured.

- Make sure while taking reading that the manometer is properly primed.

- Priming is the operation of filling the upper part of the manometer and the connecting pipes with water and venting air from the pipes.

- First open the inlet gate valve of the apparatus.

- Adjust the control valves kept at the exit end of the apparatus to a desired flow rate and maintain the flow steadily.

- Note the time required for 100mm rise in measuring tank and manometer reading. Take reading for different flow rates.

FORMULA

ACTUAL DISCHARGE

Actual rate of flow Qa = Ah/t m3/sec

Where A = Area of the measuring tank in ‘m2 ‘

h = Difference in levels of water in ‘m’ x (13.6 - 1) t = Time in ‘seconds’

THEORITICAL DISCHARGE

The Theoretical discharge through an orifice meter is given by the following formula

Qt= k √H m3/sec

The above equation is simplified from the formula.

Qt= a1a2√2gH/√ a12a22

Where a2√2g/√1-m2

a2= Area of Orifice in ‘m2’ m = Area ratio = a2/a1

h = Differential head of manometer in ‘meters’ g = Acceleration due to gravity (9.81m/sec2) a1= Inlet Area of orificemeter in ‘m2’

CO-EFFICIENT OF DISCHARGE

Co- efficient of discharge = Q a / Q t (no units) This orifice meter is designed for the following area and diameter ratios. The flow constants are given below for the Orifice meter

| orificemeter Size (mm) |  | orifice dia (mm) |  | Flow constant (k) |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 25 |  |  |  | 16.79 |  |  | 1.095 x 10-3 |  |  |  |
| Sl |  | Manometer |  |  | Manometer | Time | Actual | Theoretical | Co- |
| N |  | Reading |  |  | Head ‘h’ | for | discharge | Discharge | efficient |
| o |  | (mm of hg) |  |  | m of water | 100m | Qa | Qt | of |
|  |  |  |  |  |  | rise ‘t’ | m2/sec | m2/sec | discharg |
|  |  |  |  |  |  | sec |  |  | e cd |
| 1 | h1 | h2 | hm |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |  |  |  |

ORIFICEMETER TEST RIG DETAILS

Size of orifice meter inlet d1 = 25mm

Orifice meter diameter d2 = 16.77mm

Area ratio a2/a1 = 0.45

Measuring area in collecting tank A = 0.3 x 0.3m2

K value = a2√2g/√1-m2

RESULT

The co efficient of discharge through orifice meter is ……

FLOW THROUGH VARIABLE DUCT AREA-BERNOULLI’S EXPERIMENT

EXP NO: 04

DATE:

AIM

To verify the Bernoulli’s theorem.

APPARATUS USED

1) A supply tank of water a tapered inclined pipe fitted with no. of piezo-meter tubes point,

2) Measuring tank

3) Scale

4) Stop watch.

THEORY

Bernoulli’s theorem states that when there is a continues connection between the particle of flowing mass liquid, the total energy of any sector of flow will remain same provided there is no reduction or addition at any point.

FORMULA USED

H1= Z1+ p1/w + V12/2g

H2= Z2+ p2/w + V22/2g

PROCEDURE

- Open the inlet valve slowly and allow the water to flow from the supply tank.

- Now adjust the flow to get a constant head in the supply tank to make flow in and out flow equal.

- Under this condition the pressure head will become constant in the piezometer tubes.

- Note down the quantity of water collected in the measuring tank for a given interval of time.

- Compute the area of cross-section under the piezometer tube.

- Compute the area of cross-section under the tube.

- Change the inlet and outletsupply and note the reading.

- Take at least three readings as described in the above steps.

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Discharge

Of

piezometer

Tube from

inlet

Area of

Cross-

section

Under foot

Of each  point

Velocity

Of water

Under foot

Of each  point

V2/2g

p/ ρ

p/ ρ+

V2/2g

RESULT

- When fluid is flowing, there isa fluctuation in the height of piezometer tubes, note the mean position

carefully.

- Carefully keep some level of fluid in inlet and outlet supply tank.

FLOW THROUGH RECTANGULAR NOTCHE

EXP NO: 05

DATE:

OBJECTIVES

To determine the coefficients of discharge of the rectangular notches

APPARATUS REQUIRED

- Hydraulic bench

- Notches \

- Rectangular,

- Hook and point gauge

- Calibrated collecting tank

- Stop watch

DESCRIPTION

In open channel hydraulics, weirs are commonly used to either regulate or to measure the volumetric flow rate. They are of particular use in large scale situations such as irrigation schemes, canals and rivers. For small scale applications, weirs are often referred to as notches and invariably are sharp edged and manufactured from thin plate material. Water enters the stilling baffles which calms the flow. Then, the flow passes into the channel and flows over a sharp-edged notch set at the other end of the channel. Water comes of the channel in the form of a nappe is then directed into the calibrated collection tank. The volumetric flow rate is measured by recording the time taken to collect a known volume of water in the tank.A vertical hook and point gauge,mounted over the channel is used tomeasure the head of the flow above the crest of the notch.

FORMULAE USED

A) RECTANGULAR NOTCH

Coefficient of discharge

Actual discharge = Qa × (Theoretical discharge)

Qa =Ah/t m3/s

Throrectical discharge Qt=2/3√2gh.H3/2. m3/ s

Co efficient of discharge Cd= Qa/ Qt

PROCEDURE

PREPARATION FOR EXPERIMENT

- Insert the givennotch into the hydraulic bench and fit tightly by using boltsin order to prevent leakage.

- Open the water supply and allow water till over flowsover the notch.Stop water supply, let excess water drain through notch and note the initial reading of the water level ‘h’using the hook and point gauge.

- Let water drain from collecting tank and shut the valve of collecting tank after emptying the collecting

tank.

EXPERIMENT STEPS

- After initial preparation, open regulating valve to increase the flow and maintain water level over notch. Wait until flow is steady.

- Move hook and point gauge vertically and measure the current waterlevel ‘h1’ to find the water head ‘H’ above the crest of the notch.

- Note the piezometric reading ‘z0’ in the collecting tank while switch on the stopwatch.

- Record the time taken ‘T’ and the piezometric reading ‘z1’ in the collecting tank after allowing sufficient water quantity of water in the collecting tank.

- Repeat step 3to step 6 by using different flow rate of water, which can be done by adjusting the water supply. Measure and record the H, the time and piezometric reading in the collecting tank until sets of data have been taken.If collecting tank is full, just empty it before the step no 3.

- To determine the coefficient of discharge for the other notch.

OBSERVATION

Breadth of the rectangular notch=

Area of collecting tank (A)=

Tabulation:

RESULT

Co efficient of discharge on Rectangular notch Cd=

FLOW THROUGH TRIANGULAR NOTCH

EXP NO: 06

DATE

AIM

To determine the coefficients of discharge of the triangular and notch

APPARATUS REQUIRED

1) Hydraulic bench Notches 2) Rectangular, triangular, 3) Hook and point gauge

4) Calibrated collecting tank 5) Stop watch

FORMULA

Actual discharge Qa =Ah/t m3/s

Throrectical discharge Qt=8/15√2g.H5/2tanǿ/2. m3/s

Co efficient of discharge Cd= Qa/ Qt

PROCEDURE

- Insert the given notch into the hydraulic bench and fit tightly by using boltsin order to prevent leakage.

- Open the water supply and allow water till over flows over the notch. Stop water supply, let excess water drain through notch and note the initial reading of the water level ‘h0’using the hook and point gauge. Let water drain from collecting tank and shut the valve of collecting tank after emptying the collecting tank.

- After initial preparation, open regulating valve to increase the flow and maintain water level over notch. Wait until flow is steady.

- Move hook and point gauge vertically and measure the current water level ‘h1’ to find the water head ‘H’ above the crest of the notch.

- Note the piezometric reading ‘z0’ in the collecting tank while switch on the stopwatch.

- Record the time taken ‘T’ and the piezometric reading ‘z1’ in the collecting tank after allowing sufficient water quantity of water in the collecting tank.

Observation:

Area of the collecting tank A= Angle of the Vnotch =600

RESULT

co efficient of discharge on Triangualr notch Cd=

DETERMINATION OF FRICTION CO EFFICIENT	IN PIPES

EXP NO: 07

DATE:

AIM

To find the friction ‘f’ for the given pipe.

APPARATUS REQUIRED:

- A pipe provided with inlet and outlet and pressure tapping

- Differential u-tube manometer

- Collecting tank with piezometer

- Stopwatch

- Scale

FORMULAE

FRICTION FACTOR (f ):

f = 2 x g x d x h f / l x v2 (no unit) Where,

g = Acceleration due to gravity (m / sec2) d = Diameter of the pipe (m)

l = Length of the pipe (m)

| s.no | Hook gauge |  | Head over |  |  | Co-efficient if |
| --- | --- | --- | --- | --- | --- | --- |
|  | reading |  | the notch | Discharge |  | discharge Cd= |
|  | in(m) |  | H=H1-H2 |  |  | Qa/ Qt |
|  | Sill level | Free surface |  | actual Qa | Theoretical |  |
|  | (H1) | level(H2) |  |  | Qt |  |
| 1 |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |

v = Velocity of liquid following in the pipe (m / s)

h f = Loss of head due to friction (m) = h1 ~ h2

Where

h1 = Manometric head in the first limbs

h2 = Manometric head in the second limbs.

ACTUAL DISCHARGE

Q = A x h / t (m3 / sec)

Where

A = Area of the collecting tank (m2) h = Rise of water for 5 cm (m)

t = Time taken for 5 cm rise (sec)

VELOCITY

V = Q / a (m / sec)

Where

Q = Actual discharge (m3/ sec)

A = Area of the pipe (m2)

TABULATION:

| Sl No. | Pipe | Manometer | Loss of | Time | Discharge | Velocity | V2 | Frictional |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | dia | Reading | head | for | Q | V=Q/a | (m2/s2) | factor |
|  | d | (mm of hg) | hf | 100mm | (m3/sec) | (m/s) |  | (f) |
|  | (m) |  | (m) | rise |  |  |  |  |
|  |  |  |  | T |  |  |  |  |
|  |  |  |  | (Sec) |  |  |  |  |
| 1. | 0.025 |  |  |  |  |  |  |  |

2	0.02

3	0.015

RESULT

1. The frictional factor ‘f’ for given pipe = …………..

2. The friction factor for given pipe by graphical method = …….....

CHARACTERISTIC OF CENTRIFUGAL PUMPS

EXP NO: 08

DATE:

AIM

To study the performance characteristics of a centrifugal pump and to determine the characteristic with maximum efficiency.

APPARATUS REQUIRED

1)Centrifugal pump setup

2)Meter scale

3)Stop watch

PROCEDURE

1. Start the pump and run it in a particular head on it.

2. Open the delivery valve and maintain the required delivery head

3. Note down the reading and note the corresponding suction head reading

4. Close the drain valve and note down the time taken for 10 cm rise of water level in collecting tank

5. Measure the area of collecting tank

6. For different delivery tubes, repeat the experiment

7. For every set reading note down the time taken for 5 revolutions of energy meter disc

FORMULAE

Head (H) = (P x 10) + Vm x (13.6-1)/1000 +Z

Z = datum head = 0.7m

P = P2 – P1

Vm = Vacuum gauge reading

Q = A x h/t m3 /sec

Input = 3600 x n x 0.8/N*t

Efficiency of the motor = 0.8

Output = γ QH

Where γ = Density of water = 9.81 kN/ m3

Efficiency = Output /inputx 100

GRAPHS

| 1. Head Vs Discharge |  |
| --- | --- |
| 2. Head Vs Discharge |  |

3. Head Vs Power

`CENTRIFUGAL PUMP TEST RIG

TABULATION

| Sl.No |  | Reading GaugeVacuum | hHead | te ofrev2forTime | tm 100mmforTime | QDischarge | IPInput |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Pressure gauge reading |  |  | EM | rise |  |  |
| kg/cm2 |  |  |  |  |  |  |  |
| First | second | Vm | m | Sec | Sec | m/Sec | kW |
| stage | stage |  |  |  |  |  |  |
| 1 |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |

OP

Output

kW

Efficiency η

%

RESULT

Thus the performance characteristics of centrifugal pump was studied and the maximum efficiency was found to be _____________

CHARACTERISTIC OF RECIPROCATING PUMPS

EXP NO: 09

DATE:

AIM

To study the performance characteristics of a reciprocating pump and determine the characteristic with maximum efficiency.

APPARATUS REQUIRED

- Reciprocating Pump

- An electric motor to drive the pump.

- Belt and pulley arrangement.

- Measuring tank.

- Panel board arrangement.

- Piping system.

- Sump Tank.

PROCEDURE

1. Pour in lubricating oil SAE 20/40 in the crank of the reciprocating pump to the required level (250 cc).

2. Prime the pump and start the motor. Before starting open the delivery valve and close the gauge as a safety measure.

3. The total head is measured with the help of the pressure and vacuum gauges. The total head is the sum of the pressure gauge reading, vacuum gauges reading and the height of the pressure gauge above the vacuum gauge.

4. Discharge is the amount of liquid delivered by the pump over a definite period of time. It is usually expressed in m3/sec. The actual discharge is determined with the help of the measuring tank. The time taken for ‘h’ metre of rise in water is noted. The amount of water discharge is calculated using the formula. Flow rate = quantity of water collected in measuring tank in unit time.

5. The A.C. motor’s power input is measured with the help of the energy meter connected in the line. The time taken for ‘n’ revolutions for energy meter disc is noted. The power input is calculated using formula.

6. The output power is determined using the discharge and head of water.

7. Then the efficiency is calculated as Output	Efficiency = Output/input x 100%

FORMULAE

1. Pressure gauge reading (P) in metre of water = P in kg/cm2 x 10

2. Vacuum gauge reading (V) in metre of water = V in mm of hg/1000 x (13.6-1)

3. Datum head (Z) in metre = difference in height of pressure & vacuum gauge points = 0.6 metre 4. Total head (H) in metre = P in metres of water + V in metres of water + Z in metre = P + V + Z

5. Discharge (Q) in m3/sec = Area of measuring tank in m2 x Rise of water level (h) in metres/ Time for ‘h’ metre rise of level in seconds= Ah/t

6. Output in kW = specific weight of water in KN/m3 (9.81) x Discharge in m3/sec x Total head in Metres = γ QH

7. Piston stroke Length in the mm = 45 mm 8. Piston Diameter in mm = 40 mm.

9. Input in kW = ‘n’ revolutions of energy meter disc x 3600 x Efficiency of motor (0.8)/ Energy meter constant in Rev/kW-hr x Time for n revolutions

10. Efficiency of Pump=ourput/input*100

GRAPHS

| 1. Actual discharge Vs | Total head |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2. Actual discharge Vs | Efficiency |  |  |  |  |  |  |
| 3. Actual discharge Vs | Input power |  |  |  |  |  |  |
| 4. Actual discharge Vs | Output power |  |  |  |  |  |
| Sl.No Pressure | Vacuum | Total | Time | Discharge | Time | Input | Output | Efficiency |
| gauge | Gauge | Head | for | Q | for ‘n’ | Power | Power | η |
| reading | Reading | H | 100mm | m3/sec | rev of | IP | OP | % |
| P | V | Metres | rise |  | EM | kW | kW |  |
|  | mm of |  | T |  | disc |  |  |  |
| kg/cm2 | hg |  | Sec |  | T Sec |  |  |  |

1

2

3

4

5

RESULT

The performance characteristic of the reciprocating pump is studied and the efficiency is calculated

…………… %

CHARACTERISTIC OF GEAR PUMPS

EXP NO: 10

DATE:

AIM

To draw the characteristics curves of gear oil pump and also to determine efficiency of given gear oil pump.

APPARATUS REQUIRED

1. Gear oil pump setup

2. 1 Phase, 1 HP, 1440RPM motor

3. Reservoir tank arrangement.

- Measuring tank arrangement.

- Piping system

6. Input power measurement. Etc

PROCEDURE

1. The gear oil pump is stated.

2. The delivery gauge reading is adjusted for the required value. 3. The corresponding suction gauge reading is noted.

4. The time taken for ‘N’ revolutions in the energy meter is noted with the help of a stopwatch. 5. The time taken for ‘h’ rise in oil level is also noted down after closing the gate valve.

6. With the help of the meter scale the distance between the suction and delivery gauge is noted. 7. For calculating the area of the collecting tank its dimensions are noted down.

8. The experiment is repeated for different delivery gauge readings. 9. Finally the readings are tabulated.

FORMULAE

Q = A x h /t

H = (P x 10) + (v x 13.6)/1000 + Z

Input Power = n x 3600/ N x T ηm

Output Power = δ Q H

Efficiency (η) = Output Power/ Input Power x 100

Where

A = Area of measuring tank.

H = measuring level of water in m

t = time for measuring level for 100 mm. n = number of revolution

T = Time for number of revolution in seconds.

ηm = Efficiency of motor = 0.8

GRAPH

1. Actual discharge Vs Total head

2. Actual discharge Vs Efficiency

3. Actual discharge Vs Input power

4. Actual discharge Vs Output power

TABULATION

| Sl. | P | V | Z | H | Time | Q | Time | Input | Output | Efficiency |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| No. | kg/cm2 | hg | In | m | for 100 | m3/sec | for 3 | (kW) | (kW ) | % |
|  |  | mm | M |  | rise in |  | rev of |  |  |  |
|  |  |  |  |  | Sec(t) |  | EM |  |  |  |
|  |  |  |  |  |  |  | Sec(T) |  |  |  |
| 1 |  |  |  |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |  |  |  |  |
| 9 |  |  |  |  |  |  |  |  |  |  |
| 10 |  |  |  |  |  |  |  |  |  |  |
| 11 |  |  |  |  |  |  |  |  |  |  |
| 12 |  |  |  |  |  |  |  |  |  |  |
| 13 |  |  |  |  |  |  |  |  |  |  |

RESULT

Thus the performance characteristic of gear oil pump was studied and maximum efficiency was

found to be. ………

CHARACTERISTIC OF PELTON WHEELTURBINES

Exp No: 11

DATE:

AIM

To conduct load test on Pelton wheel turbine and to study the characteristics of Pelton wheel turbine.

APPARATUS REQUIRED

- Pelton wheel turbine

- Stopwatch

- Tachometer

- Dead weight

PROCEDURE

1. The Pelton wheel turbine is started.

2. All the weight in the hanger is removed.

3. The pressure gauge reading is noted down and it is to be maintained constant for different loads.

4. The venturimeter  readings are noted down.

5. The spring balance reading and speed of the turbine are also noted down.

6. A 5Kg load is put on the hanger, similarly all the corresponding readings are noted down.

7. The experiment is repeated for different loads and the readings are

tabulated.

FORMULA

Input Power = γ QH in kW

Where γ = Specific weight of water = 9.81 kN/m3

Q = Discharge in m3/sec.

H = Supply head in meters.

Brake Power = 2π N ReW x 9.81/ 60000 kW

Efficiency = Output/ Input x 100%

Where

N = Turbine speed in RPM.

T = Torque in kg m, (effective radius of the brake drum in meters (Re)x the net brake load in kg (W).

GRAPHS

The following graphs are drawn. 1. BHP Vs IHP

2. BHP Vs speed

3. BHP Vs Efficiency

| Sl.No Pressure | Pressure | Venturimeter | Discharge | Weight | Spring | Net | Speed | Output | Input |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| (H) | Gauge | Head |  | on | balance | load |  |  |  |
| gauge | Reading |  |  | hanger | reading |  |  |  |  |
| reading |  |  |  |  |  |  |  |  |  |
| P.S | P1 P2 P | h | Q | W1 | W2 | W | N | OP | IP |
| kg/cm2 | Kg/cm2 |  | m3/sec | kg | kg | kg | rpm | kW | kW |

1

2

3

4

5

6

PELTON TUBRINE TEST RIG 1 kW (CLOSED CIRCUIT) DETAILS:

Brake drum dia D = 0.2m

Input total head H in m of water = Pressure gauge reading in kg/cm2x 10 Venturimeter Head h in m of water = (P x 10)

Discharge Q = k √h (h in m of water) Input power IP=γ QH kW (h in m of water)

Brake Drum net load W = (W1 + weight of rope hanger) – W2 kg Turbine output OP = (2π NW Re x 9.81)/ 60000 kW

Efficiency η = (Output / Input) x 100%

Pumpset Brand & Model = CRI; 5H3 Effective radius of = (D/2 + t) = 0.115m Break drum

Weight of rope & hanger = 1kg Spear Opening = Full

Gate value Opening= Full “K” value = 3.183 x 10-2

RESULT

Thus the performance characteristic of the Pelton Wheel Turbine is done and the maximum efficiency of the turbine is ………

CHARACTERISTIC OF FRANCIS TURBINES

Exp No: 12

DATE:

AIM

To conduct load test on francis turbine and to study the characteristics of francis turbine.

APPARATUS REQUIRED

- Francis Turbine Test Rig

- Stop watch

- Tachometer

PROCEDURE

1. The Francis turbine is started

2. All the weights in the hanger are removed

3. The pressure gauge reading is noted down and this is to be Maintained constant for different loads

- Pressure gauge reading is ascended down

- The venturimeter reading and speed of turbine are noted down

6. The experiment is repeated for different loads and the reading are tabulated.

FORMULAE

VENTURIMETER READING

h = (p1 - p2) x 10 (m) Where

p1, p2 - venturimeter readings in kg / cm2

DISCHARGE

Q = 0.011 x √h (m3 / s)

BRAKE HORSEPOWER

BHP = ( x D x N x T) / (60 x 75) (h p)

Where

N = Speed of turbine in (rpm)

D = Effective diameter of brake drum = 0.315m

T = torsion in [kg]

INDICATED HORSEPOWER

HP = 1000 x Q x H / 75 (hp)

Where

H – Total head in (m)

PERCENTAGE EFFICIENCY

% = B.H.P x 100 / I.H.P ( %)

GRAPHS

The following graphs are drawn 1. BHP (vs.) IHP

2. BHP (vs.) speed

3. BHP (vs.) % efficiency

TABULATION

| Sl.No | Pressure | Pressure | ORIFICEmeter | Discharge | Weight | Spring | Net | Speed |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | (H) | Gauge | Head |  | on | balance | load |  |
|  | Gauge | Reading |  |  | hanger | reading |  |  |
|  | reading |  |  |  |  |  |  |  |
|  | P.S | P1 P2 P | h | Q | W1 | W2 | W | N |
|  | kg/cm2 | Kg/cm2 |  | m3/sec | kg | kg | kg | rpm |
| 1 |  |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |  |

FRANCIS TUBRINE TEST RIG 1 kW, 1000 RPM (CLOSED CIRCUIT) DETAILS

Brake drum dia D = 0.2m Rope Dia t = 0.015m Effective radius of = (D/2 + t) Brake drum Re = 0.115m Weight of rope & hanger = 1kg Guide vane opening =0.5

“K” value : 9.11 x 10-310-3

Input total head H in m of water = Pressure gauge reading in kg/cm2x 10 Orificemeter Head h in m of water h= (p1-p2) x 10m of water Discharge Q = K√h (h in m of water)

Input power IP=γ x H x Q kW (H in m of water)

Brake Drum net load W = (W1 + weight of rope & hanger) – W2 kg Turbine output OP = (2π NWRe x 9.81)/ 60000 kW

Efficiency η = (output / input) x 100%

PUMP MODEL: CRI; LH3

RESULT

Thus the performance charactertics of the Francis wheel turbine are done and the maximum efficiency of the turbine is …………. %

CHARACTERISTIC OF KAPLAN TURBINES

EXP NO :13

DATE	:

AIM

To study the characteristics of a Kaplan turbine

APPARATUS REQUIRED

1)Kaplan Turbine 2)Supply Pump 3)Orifice meter

4)Pressure & Vacuum Gauge 5)Sump tank

6)Piping System

PROCEDURE

1. Keep the runner vane at require opening

2. Keep the guide vanes at required opening

3. Prime the pump if necessary

4. Close the main sluice valve and them start the pump.

5. Open the sluice valve for the required discharge when the pump motor switches from star to delta mode.

6. Load the turbine by adding weights in the weight hanger. Open the brake drum cooling water gate valve for cooling the brake drum.

7. Measure the turbine rpm with tachometer

8. Note the pressure gauge and vaccum gauge readings

9. Note the orifice meter pressure readings.

10. Repeat the experiments for other loads.

FORMULAE

Input Power = γ QH in kW

Where γ = Specific weight of water = 9.81 kN/m3

Q = Discharge in m3/sec.

H = Supply head in meters.

Brake Power = 2π NT x 9.81/ 60000 kW Efficiency = Output/ Input *100% Where

N = Turbine speed in RPM.

T = Torque in kgm, (effective radius of the brake in meters (R)x The net brake load in kg (W). Re = 0.165m

GRAPHS

The following graphs are drawn.

1. BHP Vs IHP

2. BHP Vs speed

3. BHP Vs Efficiency

KAPLAN TUBRINE TEST RIG 1 kW, 1000 RPM (CLOSED CIRCUIT) DETAILS

Brake drum dia D = 0.3m

Input total head H in m of water = Pressure gauge reading in kg/cm2x 10

Orificemeter Head p in m of water h= (p1-p2) x 10

Discharge Q = K√p (h in m of water)

Input power IP=γ x H x Q kW (H in m of water)

Brake Drum net load W = (W1 + weight of rope & hanger) – W2 kg

Turbine output OP = (2π NWRe x 9.81)/ 60000 kW

Efficiency η = (output / input) x 100%

Rope Dia t = 0.015m

Effective radius of = (D/2 + t) = 0.165m

Weight of rope & hanger = 1kg

Guide vane opening =0.8 Run away speed = 1750RPM “K” value = 2.3652 x 10-2

Pumpset Brand & Model = CRI;1

| Sl.No | Pressure | Orificemeter | ORIFICEmeter | Discharge | Weight | Spring | Net | Speed | Output | Input | Efficiency |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | (H) | head Pressure | Head |  | on | balance | load |  |  |  |  |
|  | gauge | Gauge |  |  | hanger | reading |  |  |  |  |  |
|  | reading | Reading |  |  |  |  |  |  |  |  |  |
|  | P.S | P1 P2 P | H | Q | W1 | W2 | W | N | OP | IP | η |
|  | kg/cm2 | Kg/cm2 |  | m3/sec | kg | kg | kg | rpm | kW | kW | % |
| 1 |  |  |  |  |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |  |  |  |  |

RESULT

Thus the performance characteristic of the Kaplan Turbine is done and the maximum efficiency of the turbine is ………. %